Nodes: These are software processes that do 'stuff' (e.g. process data, command hardware, execute algorithms). Nodes provide modularity to robotic projects that use ROS. They are often written in C++ or Python. In this, we will use Python to write them. ROS is only compatible with Python 2.7.x. Topics: Transport information between nodes, in the form of messages. In a real robot application you will often have to deal with a large number of nodes and topics. It is important to know which nodes are talking to each other, and what topics are being used to pass the information (messages) between nodes.
Don't forget to source your workspace if you want to use ROS commands!
If you've followed the procedure under the Course Setup section correctly, you only need to execute the following in the shell: $ source $HOME/hrwros_ws/devel/setup.bash
Summary:
There are three main ways to inspect a ROS node:
Simply list all currently running nodes in the terminal:
rosnode list
Make a visual graph of all running nodes and their connections:
rqt_graph
List information about a specific node in the terminal:
rosnode info <node_name>
In the following lectures, we will learn much more about Nodes. For example, we will see that they can publish (write) to a topic and subscribe (read) from a topic.
ROS topics transport information between nodes. This information is organized as a data structure and can have different data types. Topics can be identified by their name and their type. You can think of topics as strongly typed message buses. Any node can connect to it to send or receive data, as long as they are the right type.
As with nodes, there are three ways to inspect topics:
Don't forget to source your workspace if you want to use ROS commands! If you've followed the procedure under the Course Standards section correctly, you only need to execute the following in the shell: $ source $HOME/hrwros_ws/devel/setup.bash
Display a list of all topics that are currently being exchanged between active nodes list
- Display information about the data structure of a specific topic
  rostopic info <topic_name>
- Print the current content of a topic in the terminal
  rostopic echo <topic_name>
Important detail: Do not forget the "/" before node and topic names!
It's time to build your own ROS application structure! There are four fundamental types of ROS nodes that can be used to build a ROS application:
- Publishers
- Subscribers
- Services
- Actions
Please keep in mind, that here we refer to Services and Actions as fundamental types of nodes. That is, we are referring to nodes that use services and actions for communication. Publishers, Subscribers, Services and Actions are used by ROS nodes to communicate between each other.
First, we will focus on Publisher and Subscriber nodes.
Publisher Nodes
A ROS node that generates information is called a publisher. A publisher sends information to nodes via topics. With robotics often these publishers are connected with sensors like cameras, encoders, etc.
If you use rosnode info you can see to which topics a node is connected, and if these are outbound or inbound connections.
Subscriber Nodes
A ROS node that receives information is called a subscriber. It's subscribed to information a topic and uses topic callback functions to process the received information. With robotics, subscribers typically monitor system states such as triggering an alert when the robot reaches joint limits.
You can again use rosnode info to find information about a subscriber node. Don't forget to source your workspace!
PUBLISHER:

## Node to publish a string topic.
import rospy
from std_msgs.msg import String

def simplePublisher():
    simple_publisher = rospy.Publisher('topic_1', String, queue_size = 10)
    rospy.init_node('node_1', anonymous = False)
    rate = rospy.Rate(10)

    # The string to be published on the topic.
    topic1_content = "my first ROS topic"

    while not rospy.is_shutdown():
        simple_publisher.publish(topic1_content)
        rate.sleep()

if __name__== '__main__':
    try:
        simplePublisher()
    except rospy.ROSInterruptException:
        pass
SUBSCRIBER:

## Node to subscribe to a string and print the string on terminal.

import rospy
from std_msgs.msg import String

# Topic callback function.
def stringListenerCallback(data):
    rospy.loginfo(' The contents of topic1: %s', data.data)

def stringListener():
    rospy.init_node('node_2' , anonymous = False)

    rospy.Subscriber('topic_1' , String, stringListenerCallback)

    # spin() simply keeps python from exiting until this node is stopped
    rospy.spin()

if __name__ == '__main__':
    stringListener()

ROS file system - nomenclature
ROS workspace (catkin workspace) consists of different subspaces. A workspace is a folder to organize ROS project files. ROS uses catkin, which is a build tool to compile source files into binary files. Your code goes into the src workspace folder and catkin manages the other ones. A catkin ROS workspace contains three main spaces:
src space: contains source code, this will be your main work folder;
devel space: contains setup files for the project ROS environment;
build space: contains the compiled binary files
If you'd like to read some more about these spaces.
We will now guide you through the creation of our own catkin workspace in ROS. This workspace will just be used as an example to show you the process, and won't be used anymore after this.
First, create a new folder for your workspace: $ mkdir -p new_ros_ws/src
You can use ls to verify the new folder that was created. Next move to your newly created workspace using the cd new_ros_ws Thereafter, the correct ROS environment using the source /opt/ros/melodic/setup.bash Finally, we initialize catkin:
$ catkin init;
$ catkin build;
##### Warning!
If you independently follow the tutorials on ROS Wiki, you might come across the command catkin_make. That is different to what we use in our course which is catkin. Don't try and mix the two!
ROS packages in the 'src' space. In ROS, software is organised in ROS packages. A ROS package typically contains the following things:
- CMakeList.txt
- package.xml(These two files indicate that the folder is a ROS package file. More on these two later in the course)
- scripts/(This folder contains all Python scripts. We will only use Python in this course)
- src/(This folder contains all C++ source files. We will not use these in this course)
To create a new ROS package, we will use catkin:
$ cd <path_to_ros_ws>/src
$ catkin_create_pkg hrwros_week2 std_msgs
Please keep in mind that you don't need to place the source files of any dependencies, such as std_msgs in the line above. Instead, you can simply install their binaries with the rosdep command:
$ install <package_name>
You can also install all ROS package dependencies in one command:
$ cd <path_to_ros_ws>/src
$ rosdep install --from-paths . --ignore-src -y
src is not the only space in your workspace: there is also the 'devel' space. This contains all binary executables from src.
Nodes can process and share information through topics. The information they pass through these topics needs to be structured in some way, to make it actually usable. Such a structure is known as a data structure. In ROS, we can abstract these data structures as ROS message types. Common data structures in ROS are for example floats, integers, and strings.
In ROS, we can easily combine multiple data structures using derived message types. For example, to represent a position in 3D space we will need 3 floating point values: X, Y and Z. The derived message type will then be a struct of three floating point numbers: {float x, float y, float z}.
These (derived) message types are defined in message files. These message files are typically located in <ros_package_name>/msg, with the filename <NewMessageType>.msg. For example, look in the $HOME/hrwros_ws/src/hrwros/hrwros_msgs/msg folder for some examples.
#### Example: Ultrasound distance sensor.
We want to construct a new message type SensorInformation It should contain:
- message type for interfacing with distance sensors
- A string containing the manufacturer name
- An unsigned integer containing the sensor part number
We would create the following file:
$HOME/hrwros_ws/src/hrwros/hrwros_msgs/msg/SensorInformation.msg.
It will contain the following:
sensor_msgs/Range sensor_data
string maker_name
uint32 part_number
We can see something really interesting here: We use an already derived message, sensor_msgs/Range, and simply add a string and an integer to it. So we can create new message types using already existing derived message types! This idea of stacking is really useful in ROS, since you can easily re-use what already exists. So in the above example, the sensor_msgs/Range already contains everything we need from the range sensor itself, and we only add the maker name and the part number.

1.	Publisher, Subscriber and Custom Message Type: THE PROCESS
Ok, we have ROS nodes in a ROS application. And nodes process information. And the information is organized as data structures. These data structures are called ROS message types. And, nodes use topics to talk to each other and exchange information. Therefore, topic type is just an abstract concept. A topic just carries whatever information the nodes want a topic to carry. So, if the same nodes exchange a different kind of information, the topic can carry that information. In essence, topic types are just abstract concepts and they acquire or inherit the ROS message type that they are asked to carry by the ROS nodes.
1.1.	CREATING A NEW MESSAGE TYPE
1. Using ‘roscd <msg_folder>’ to acess workspace msg;
2. Then we go to the msg folder with ‘cd msg’ or mkdir msg;
3. Inside <msg_folder>/msg create message file, like: SensorInformation.msg with ‘touch SensorInformation.msg’;
4. With ‘rosmsg show <ROS_msg_type>/’ can visualize all message types direct linked with the tapped <ROS_msg_type>, like: ‘rosmsg show sensor_msgs/’
  Obs. If you use any type of predefined msg from ROS, is know that you should keep the message template open for your guide in msg constructing;
5. After all, define the message construct. Inside SensorInformation.msg folder, like: Format → Variable type, like String, uint32, ROS type, etc. And Variable name. Formate a pair: [Variable Type, Variable Name]. So, SensorInformation.msg looks like: {sensor_msgs/Range sensor_data; string maker_name; uint32 part_number};
6. Add the new message type ‘SensorInformation.msg’ inside CmakeList.txt in the ‘add_message_files()’ function;
7. After all configurate, the result appear:
- Inside the Workspace (We call it hrwros_ws):
  - Path: hrwros_ws / src / hrwros / hrwros_msgs
  - Folders inside Hrwros_msgs: msg, CmakeList.txt, package.xml.
  - And, at least, make catkin build command, wich creates a importable	python objects for the new message type.
  - So, for check if all be done verify if the menssage escope has been defined. With: ‘rosmsg hrwros_msgs/SensorInformation’

1.2.	CREATING A PUBLISHER NODE
1. Using ‘roscd <Nodes_folder>’ to acess workspace that contain scripts folder;
2. The files looks like: CMList.txt, launch, package.xml, scripts;
3. Inside <Nodes_Folder>/script create the publisher node file, with ‘touch sensor_info_publiser.py’;
4. Then, use the previous Publisher template for copy this inside of new sensor_info_publiser, like: ‘cp template_publisher_script.py sensor_info_publiser.py’;

- ## Node to publish a string topic.
- import rospy
- #from std_msgs.msg import String
- from hrwros_msgs.msg import SensorInformation
- from hrwros_utilities.sim_sensor_data import distSensorData as getSensorData
- def sensorInfoPubliser():
- si_publisher = rospy.Publisher('sensor_info', SensorInformation, queue_size = 10)
- rospy.init_node('sensor_info_publiser', anonymous = False)
- rate = rospy.Rate(10)
- # Create a new SensorInformation object and fill it contents.
- sensor_info = SensorInformation()
- # Fill in the header formation
- sensor_info.sensor_data.header.stamp = rospy.Time.now()
- sensor_info.sensor_data.header.stamp = ‘distance_sensor_frame’
- # Fill in the sensor data information
- sensor_info.sensor_data.radiation_type = sensor_info.sensor_data.ULTRASOUND
- sensor_info.sensor_data.field_of_view = 0.5
- sensor_info.sensor_data.min_range = 0.02
- sensor_info.sensor_data.max_range = 2.0
- # Fill in manufacture name and part number
- sensor_info.maker_name = ‘The ultrasound company’
- sensor_info.part_number = ‘123456’
- while not rospy.is_shutdown():
- # Infinite loop for refeed the values
- sensor_info.sensor_data.range = getSensorData( sensor_info.sensor_data.radiation_type, sensor_info.sensor_data.min_range, sensor_info.sensor_data.max_range )
- # Publish the sensor information on the /sensor_info topic
- si_publisher.publish(sensor_info)
- rate.sleep()
- if __name__== '__main__':
- try:
- sensorInfoPublisher()
- except rospy.ROSInterruptException:
        pass
5.	The ‘rospy.Publisher()’ function receive two main	arguments: Topic Name and Message Type, like:	rospy.Publisher(TopicName, MessageType, queue =	10). So, rospy.Publisher(sensor_info,	SensorInformation, queue = 10). It mean that this script	create a new topic	called ‘sensor_info’ that can be	published (writable) with message in SensorInformation	types.
6.	The ‘rospy.init_node()’ function receive one main	argumet: Node name. Like:	rospy.init_node(NodeName, anonymous = False). So,	rospy.init_node(sensor_info_publisher, anonymous =	False). It mean that this script define a new name for this	specific node called ‘sensor_info_publisher’ that can be	discovery for anyother nodes, with no-anonymous mode.
7.	Create a new Object that reference for new message	type, so: The topic ‘sensor_info’ has a message type ‘	SensorInformation’ → sensor_info =	SensorInformation(). According of message type	SensorInformation is necessary populate the specfic	field of respective data information. The type of	‘SensorInformation’ is:
1. sensor_msgs/Range sensor_data
                  uint8 ULTRASOUND=0
  uint8 INFRARED=1
  std_msgs/Header header
  uint32 seq
  time stamp
  string frame_id
  uint8 radiation_type
  float32 field_of_view
  float32 min_range
  float32 max_range
  float32 range
2. string maker_name
3. uint32 part_number
      What its mean? So, sensor_data is an Object with sensor_msgs/Range type. And it have that structure:
      1. sensor_data = {
        1. ULTRASOUND,
        2. INFRARED,
        3. header = {
        4. seq,
        5. stamp,
        6. frame_id
        7. },
        8. radiation_type,
        9. field_of_view,
        10. min_range,
        11. max_range,
        12. range
      2. },
      3. maker_name,
      4. part_number
            And each proprierty of that object can be acessed by: sensor_info.sensor_data.<name_of_proprierty>, like: sensor_info.sensor_data.min_range or sensor_info.sensor_data.header.stamp;
  8.	Make the infinite call of the refeed function:	getSensorData();
  9.	And, alfter all initialize the sensorInfoPublisher().
  10.	Starting the system: ‘ros core’, in new terminal: ‘ros run hrwros_week1 sensor_info_publisher.py’ [rosrun will locate PACKAGE and try to find an executable named EXECUTABLE in the PACKAGE tree.]
  11.	Possibles erros: Not executable python script → make	the command: ‘chmod +x sensor_info_publisher.py’;	No module to import Called ‘SensorInformation’ →	change	import std_msgs.msg to hrwros_msgs.msg;
12.	Check topic available: rostopic list → (…) /sensor_info
13.	And finally, rostopic echo /sensor_info to view the datas refresh.
So: Remainder →
#### Preparing your script file
If you've entered a new CCS, don't forget to source your workspace if you want to use ROS commands! If you've followed the procedure under the Course Setup section correctly, you only need to execute the following in the shell:
source $HOME/hrwros_ws/devel/setup.bash
Let's first navigate to our Week 1 workspace folder: $ roscd hrwros_week1
Enter the scripts folder: $ cd scripts
Then, create our node python script: $ touch sensor_info_publisher.py
We can now copy the contents of the template file template_publisher_script.py to our new python script: $ cp template_publisher_script.py sensor_info_publisher.py
We can now start modifying our new publisher node.
#### Editing your script file
For editing our script file you can use any text editor on Linux (like nano/gedit/etc.) like with the following command outside the CCS: $ gedit sensor_info_publisher.py
First, change the last line of the header comment to ensure its consistency. Import our newly created message type SensorInformation which is possible because we executed the catkin build command.
Give the function a relevant name, for example, SensorInfoPublisher.
We do the same for the Publisher object. rospy.publisher takes in the topic name and a message type. In this case, we will use 'sensorinfo' and SensorInformation Now give the node a meaningful name.
Create a new SensorInformation object and fill in its contents.
sensor_info = SensorInformation()
Fill in the header information with the timestep and distance data of the sensor.
sensor_info.sensor_data.header.stamp = rospy.Time.now()
sensor_info.sensor_data.header.frame_id = 'distance_sensor_frame'
Now Fill in the sensor data information. There you can determine the minimum and maximum range of the sensor.
sensor_info.sensor_data.radiation_type = sensor_info.sensor_data.ULTRASOUND
Fill in the manufacturer name and part number.
sensor_info.maker_name = 'The Ultrasound Company'
sensor_info.part_number = 123456
Sensor data needs to be updated frequently. Therefore a loop is necessary.	sensor_info.sensor_data.range = getSensorData
Publish the updated sensor data on this sensor_infor topic.
si_publisher.publish(sensor_info)
Let's call the correct function in the if loop. sensorInfoPublisher()
#### Starting your new ROS node
roscore a CCS after sourcing the setup files. Then, in another CCS, the ROS node with the following command, after sourcing the setup files:
$rosrun hrwros_week1 sensor_info_publisher.py
This will lead to an executable error. This error can be resolved by a simple command which makes the node executable.
$ roscd hrwros_week1/scripts
$ chmod +x sensor_info_publisher.py
Try running the ROS node with the previous command. This will lead to an import error. This is due to an incorrect message definition. We can change this with the gedit editor.
$ gedit sensor_info_publisher.py
There we need to change std_msgs.msg to hrwros_msgs.msg.
Try to run the node again. Which leads to a third error, the getSensorData function is not known. For that reason, we always need to tell python where we got functions which means it is necessary to import the utilities. So we add the following with the gedit editor in	sensor_info_publisher.py.
from hrwros_utilities.sim_sensor_data import distSensorData as getSensorData
Now you can run the ROS node without errors.
#### Inspecting our node
This node is a publisher, publishing to a topic. So let's see if we can find the topic.
$ rostopic list (we look for/sensor_info topic)
Let's look at its contents. $ rostopic echo /sensor_info
It's always nice to receive some acknowledgement that a ROS node is working. To do that we open our node in the gedit editor. $ gedit sensor_info_publisher.py
After publishing our topic we print a log message by adding the following linen of code to the file: rospy.loginfo('All went well. Publishing topic')

1.3.	CREATING A SUBSCRIBER NODE WITH A CUSTOM MESSAGE TYPE
1. Using ‘roscd <Nodes_folder>’ to acess workspace that contain scripts folder;
2. The files looks like: CMList.txt, launch, package.xml, scripts;
3. Inside <Nodes_Folder>/script create the publisher node file, with ‘touch sensor_info_subscriber.py’;
4. Then, use the previous Publisher template for copy this inside of new sensor_info_subscriber, like: ‘cp template_subscriber_script.py sensor_info_subscriber.py’;
- ## Node to subscribe to sensor information topic and print distance data.
- import rospy
- from hrwros_msgs.msg import SensorInformation
- # Topic callback function.
- def sensorInfoCallback(data):
- rospy.loginfo(' Distance reading from the sensor is: %f', data.sensor_data.range)
- def sensorInfoListener():
- rospy.init_node('sensor_info_subscriber’ , anonymous = False)
- rospy.Subscriber('sensor_info' , SensorInformation, sensorInfoCallback)
- # spin() simply keeps python from exiting until this node is stopped
- rospy.spin()
- if __name__ == '__main__':
- sensorInfoListener()

So, REMAINDER →
Start a new CCS and source the workspace setup files.
Use the template and start editing it. We will first create a new file, and copy the contents of the example file into it.
$ roscd hrwros_week1/scripts
$ touch sensor_info_subscriber.py
$ cp template_subscriber_script.py sensor_info_subscriber.py
Next, we will take a look inside our new file. Open it in your favourite editor, and follow along with the lines we indicate.
Import sensor information: from hrwros_msgs.msg import SensorInformation
Then give a meaningful names and log message:
rospy.init_node('sensor_info_subscriber', anonymous=False)
rospy.Subscriber('sensor_info', SensorInformation, sensorInfoCallback)
sensorInfoListener()
Make the subscriber script executable: chmod +x sensor_info_subscriber.py
To run our new subscriber node:
Run roscore in a new course command shell. Remember you need to source your workspace in every new shell!
$ source $HOME/hrwros_ws/devel/setup.bash
$ roscore
Then, in a separate CCS:
$ source $HOME/hrwros_ws/devel/setup.bash
$ rosrun hrwros_week1 sensor_info_subscriber.py
Check with rostopic list: $ rostopic info /sensor_info
Note: Inspect the topic with the rostopic info when debugging your ROS problems.
To actually see the contents of the topic, you will need to publish it from a new CCS.
$ rosrun hwros_week1 sensor_info_publisher.py

2.	CREATING SERVICES:
So far, communications between nodes have been handled by topics. Topics can connect many nodes to many other other nodes. There are no acknowledgements between the nodes: they are simply pumping around information. This is very useful when monitoring certain values, but can become problematic with some types of information such as video data. In cases like those, it would be nice to only receive information when requested.
ROS services implement these request-response type of communications. They consist of two message types: One for requesting data, and one for the response. These services are the gateway to event-based ROS executions. Services are defined in the same package as messages, in their own/srv folder. The nomenclature for ROS services: One ROS node is the service server. It advertises a service, and makes it available to other nodes. Another node is the service client. It sends a request message to the service server once the service is available.
#### Example
A useful example of a ROS service could be a service that converts measurements in metres to measurements in imperial feet. The request message would contain the measurement in metres, and the response would contain the measurement in imperial feet plus a boolean value indicating the conversion was successful. We would create the file hrwros_msgs/srv/ConvertMetresToFeet.srv:
1. Using ‘roscd <services_folder>’ to acess workspace services;
2. Then we go to the ‘srv’ folder with ‘cd srv’ or mkdir srv;
3. Inside <services_folder>/srv create service file, like: ConvertMetresToFeet.srv with ‘touch ConvertMetresToFeet.srv’;
4. Inside ‘CovertMetresToFeet.srv’:
- float64 measurement_metres # Request field
- --- # Demarcation between request and response
- float64 measurement_feet # Response field
- bool succes
1. Add the new service ‘CovertMetresToFeet.srv’ inside CmakeList.txt in the ‘add_service_files()’ function;
2. Inside the Workspace (We call it hrwros_ws):
  1. Path: hrwros_ws / src / hrwros / hrwros_msgs
  2. Folders inside Hrwros_msgs: msg, srv, CmakeList.txt, package.xml.
  3. And, at least, make catkin build command, wich creates a importable	python objects for the new message type.
  4. So, for check if all be done verify if the services escope has been defined. With: ‘rossrv show hrwros_msgs/ConvertMetresToFeet’
3. Create a Client-Server Scripts:
  1. Server:
- #!/usr/bin/env python
- # This code has been adapted from the ROS Wiki ROS Service tutorials to the context
- # of this course.
- # (http://wiki.ros.org/ROS/Tutorials/WritingServiceClient%28python%29)
- from hrwros_msgs.srv import ConvertMetresToFeet, ConvertMetresToFeetRequest, ConvertMetresToFeetResponse
- import rospy
- import numpy as np
- _CONVERSION_FACTOR_METRES_TO_FEET = 3.28 # Metres -> Feet conversion factor.
- # Service callback function.
- def process_service_request(req):
- # Instantiate the response message object.
- res = ConvertMetresToFeetResponse()
- # Perform sanity check. Allow only positive real numbers.
- # Compose the response message accordingly.
- if(req.distance_metres < 0):
- res.success = False
- res.distance_feet = -np.Inf # Default error value.
- else:
- res.distance_feet = _CONVERSION_FACTOR_METRES_TO_FEET * req.distance_metres
- res.success = True
- for test_idx in range(0,10):
- rospy.sleep(1)
- #Return the response message.
- return res
- def metres_to_feet_server():
- # ROS node for the service server.
- rospy.init_node('metres_to_feet_server', anonymous = False)
- # Create a ROS service type.
- service = rospy.Service('metres_to_feet', ConvertMetresToFeet, process_service_request)
- # Log message about service availability.
- rospy.loginfo('Convert metres to feet service is now available.')
- rospy.spin()
- if __name__ == "__main__":
- metres_to_feet_server()

2. Client:
#!/usr/bin/env python
- #!/usr/bin/env python
- # This code has been adapted from the ROS Wiki ROS Service tutorials to the context
- # of this course.
- import sys
- import rospy
- from hrwros_msgs.srv import ConvertMetresToFeet, ConvertMetresToFeetRequest, ConvertMetresToFeetResponse
- def metres_to_feet_client(x):
- # First wait for the service to become available.
- rospy.loginfo("Waiting for service...")
- rospy.wait_for_service('metres_to_feet')
- try:
- # Create a service proxy.
- metres_to_feet = rospy.ServiceProxy('metres_to_feet', ConvertMetresToFeet)
- # Call the service here.
- service_response = metres_to_feet(x)
- print("I only got here AFTER the service call was completed!")
- # Return the response to the calling function.
- return service_response
- except rospy.ServiceException, e:
- print "Service call failed: %s"%e
- if __name__ == "__main__":
- # Initialize the client ROS node.
- rospy.init_node("metres_to_feet_client", anonymous = False)
- # The distance to be converted to feet.
- dist_metres = 0.25
- rospy.loginfo("Requesting conversion of %4.2f m to feet"%(dist_metres))
- # Call the service client function.
- service_response = metres_to_feet_client(dist_metres)
- # Process the service response and display log messages accordingly.
- if(not service_response.success):
- rospy.logerr("Conversion unsuccessful! Requested distance in metres should be a positive real number.")
- else:
- rospy.loginfo("%4.2f(m) = %4.2f feet"%(dist_metres, service_response.distance_feet))
- rospy.loginfo("Conversion successful!")
    metres_to_feet_server()
#### Setting up the service definition files
Let's begin by sourcing our setup files, and navigate to our workspace msgs folder:
$ source $HOME/hrwros_ws/devel/setup.bash
$ roscd hrwros_msgs/
We can see the msg/ folder, but we just learned services are defined in the srv/ folder. So let's create that, and create our service file:
$ mkdir srv
$ cd srv
$ touch ConvertMetresToFeet.srv
Now our service file is created, we can start editing it. Remember, we first want the request message type, then a demarcation of three dashes, and then a response message type:
float64 distance_metres # Request message: Distance in (m) to be converted to (ft)
--- # Demarcation
float64 distance_feet # Response message: Distance in (ft) after conversion
bool success # Response message: Success or failure of conversion
Now, just like we did for messages, we add our new service to the CMakeLists.txt file in the hrwros_msgs/ folder. Note that services have their own section, after messages. Add the name of our new service definition file after the FILES entry. Don't forget the .srv file extension.
Finish by building our service by running the catkin b command. We can check if it worked correctly by using the rossrv command:
$ rossrv show hrwros_msgs/ConvertMetresToFeet
$ rossrv show hrwros_msgs/ConvertMetresToFeet -r
The terminal should show the request message field, and the response message field.
#### Inspecting our service server code:
Now we've created a new service, we can use it in our code. Let's go to the week 1 script folder, where we already have two template implementations. Let's begin by inspecting the server: metres_to_feet_server.py.
We are importing the newly created service definitions from hrwros_msgs.srv. Note that we not only have to import the service definition, but also explicitly the request and response message definitions.
The service request is processed in the service callback function.
- We first create an object for the response message type, and in the example, do a check in the distance input to check if it is a positive real number.
- If the sanity check fails, we return a default error value in the response.
- Otherwise, we do the conversion and return both the converted value and a flag that indicates the conversion was successful.
- In either case, we return the response.
Then, we have the next function for the administrative settings of the service server node.
- Here, we create a ROS node for our service.
- We create the actual service by giving it a name, a type, and a callback function for processing a service request.
- Finally, in the main function we start the service server node.
#### Inspecting our service client code
We will now be looking at the service client example: metres_to_feet_client.py.
Lines 6 through 8 contain all the required imports, and the client definition on. We first wait for the required service to become available. Then, we create a service proxy to be able to call the service. Then, we actually call the service on , and return the service response from the service call.
In the main function, we have the ROS node for the service client . We send a test value to the server via the client. Once we have a response, we check if the conversion was successful, and report the return value accordingly. We are using the logerr function for error messages .
#### Using the service server & client
First, make sure you are in the hrwros_msgs folder. Start roscore in a separate terminal. Then, source our setup files and run our server, and:
$ $HOME/hrwros_ws/devel/setup.bash
$ rosrun hrwros_week1 metres_to_feet_server.py
The service is now available. Time to also start the ROS client in a separate terminal:
$HOME/hrwros_ws/devel/setup.bash
$ rosrun hrwros_week1 metres_to_feet_client.py
The terminal will both display the request and response messages.
We learned, that services will block execution. Let's look at that as well. Since the processing, which is blocking, is happening in the server, let's go to the server file and add a delaying test loop. In metres_to_feet_server.py, navigate to #L27 and add the followingblock of code:
for test_idx in range(0,10):
rospy.sleep(1)
On the client side, let's write a log message after the response has been received. In metres_to_feet_client.py, navigate to #L21 and add the following block of code:
print('I only got here AFTER the service call was completed!')
First, terminate the server in the terminal (CTRL+C), and restart it. Restart the client the same way. You will now see the client will only print out every 10 seconds, because the processing is not complete yet on the server side.
To test: 1. ‘roscore’; 2. ‘rosrun hrwros_week1 metres_to_feet_server.py’; 3. ‘rosrun hrwros_week1 metres_to_feet_client.py’.
3.	ROS ACTIOS:
We don't always want blocking execution. ROS Actions allow non-blocking execution. This way, multiple things can happen at the same time. They are a generalized request-response system (as for services): a client-server infrastructure. Actions are defined by three message types:
1. A goal (request),
2. The result (response),
3. And feedback.
There are a few ROS commands to interact with actions:
Generate action messages manually:
$ rosrun actionlib_msgs genaction.py <path_to_action_file>
Show the contents of an action message:
$ rosmsg show <stack_name>_msgs/<ActionMessage>
ROS actions have a few functions available to process requests:
- The goalCallback function processes a goal request.
- Goal statuses: ACTIVE, SUCCEEDED, ABORTED.
Nomenclature:
- Action server: A ROS node that advertises an action, so that other nodes can request action goals to be processed.
- Action client: A ROS node that sends goal requests to the action server.
#### Code example
Here, we will show the general structure of an action file.
Requirement: Counter with a 1s delay between each increment.
- Goal message: Number to count up to (uint32);
- Result message: A status message (string);
- Feedback message: The number of counts completed (uint32);
uint32 num_counts # Goal field
--- # Separator
string result_message # Result field
--- # Separator
uint32 counts_elapsed # Feedback field

Specified actions:
1) CounterWithDelayFeedback
2) CounterWithDelayGoal
3) CounterWithDelayResult
Additional actions which are used internally by the actionlib package:
4) CounterWithDelayActionFeedback
5) CounterWithDelayActionGoal
6) CounterWithDelayAction
7) CounterWithDelayActionResult
CounterWithDelayAction.msg is an aggregation of the other action messages. This is the action type of our action client.
The action client code is something that we as users develop to leverage the facilities of the actionlib ROS package.
Sent goals are registered by the action server and the actionlib package. The package requires additional information which is CounterWithDelayAction.msg.
contains:
1. Timestamp and header info;
2. Unique goal identifier;
3. Goal message.
Action Result contains:
1. Timestamp and header info;
2. Different states the goal can be in;
Feedback contains:
1. Timestamp and header info;
2. Different states the goal can be in;
3. Feedback message.
Action server topics
- Feedback topic is published by the action server an has action feedback message type;
- Action server subscribers to the cancel topic and is of the GoalID type.
Attention!
- Simple Action Server/Client.
- Non-blocking execution of ONE goal at a time.
- New goal to the same action server will pre-empt an active goal. Meaning that the active goal is completed first before a new goal will be processed.
- n action file
Let's first create our action folder and our new action file.
$ mkdir action
$ cd action
$ nano CounterWithDelay.action
We first define the goal message as the number of counts to count up to. Then a result message which is a message for the result and a feedback message to indicate the numbers of counts elapsed.
uint32 num_counts
---
string result_message
---
uint32 counts_elapsed

Now we update the CMakeLists.txt file with the vim editor in the action files subsection.
CounterWithDelay.action
We need to add the actionlib package that provides all the ROS action functionalities. Weneed to add it at all dependancy locations.
actionlib actionlib_mgs
Update the package.xml file also with the dependency. (#L21)
Now run catkin build or in short catkin b.
#### Action message
Don't forget to source your ROS workspace first!
$ source $HOME/hrwros_ws/devel/setup.bash
If we type the complete action
$ rosmsg showhrwros_msgs/CounterWithDelayAction will see the complete message definition.
We need to pay attention to where our message definitions are located as a lot of the message is for the package. If you want to see the message definition, you can go to the hrwros_msgs package folder.
$ roscd hrwros_msgs
And run the following script.
$ rosrun actionlib_msgs genaction.py -o msg action/CounterWithDelay.action
There we find all the action definitions.
$ rosmsg show hrwros_msgs/

Similar to the services in the previous module we have the action server and the action client. This example script has been modified from the tutorial on the ROS wiki to suit this course context.
The relevant imports and the python class implementation of the action server.
Followed by the defined feedback and messages. Then we initialise the action server. After that, we start theaction server with the start function. Now the execute callback function needs to be configured. In the final part, we first create the ROS node for the action server. Then we instantiate the action server implementation by initialisingit with the name of the node.
Now to the action client. First, you have the imports followed by a simple action client. After that, you wait for the server to become available. Then we create a goal message. We can include a blocking functionality or performother actions while the action is being processed. Lastly, we return the result.
Actions in action!
Don't forget to source your workspace in every shell first!
$ source $HOME/hrwros_ws/devel/setup.bash
roscore a different terminal.
Then we start the action server and client with the following commands.
$ rosrun hrwros_week1 counter_with_delay_as.py
$ rosrun hrwros_week1 counter_with_delay_ac.py
You can see while the goal is being progressed you can do other things. We can verify this with the following code.
$ rostopic echo /counter_with_delay/feedback
Python Action-Server:
- #! /usr/bin/env python
- # This code has been adapted from the ROS Wiki actionlib tutorials to the context
- # of this course.
- # (http://wiki.ros.org/hrwros_msgs/Tutorials)
- import rospy
- import actionlib
- from hrwros_msgs.msg import CounterWithDelayAction, CounterWithDelayFeedback, CounterWithDelayResult
- class CounterWithDelayActionClass(object):
- # create messages that are used to publish feedback/result
- _feedback = CounterWithDelayFeedback()
- _result = CounterWithDelayResult()
- def __init__(self, name):
- # This will be the name of the action server which clients can use to connect to.
- self._action_name = name
- # Create a simple action server of the newly defined action type and
- # specify the execute callback where the goal will be processed.
- self._as = actionlib.SimpleActionServer(self._action_name, CounterWithDelayAction, execute_cb=self.execute_cb, auto_start = False)
- # Start the action server.
- self._as.start()
- rospy.loginfo("Action server started...")
- def execute_cb(self, goal):
- counter_delay_value = 1.0
- ## Assignment 3 - Part3
- ## modify counter delay using a private parameter .
- ## Uncomment the following lines (37-41) and modify them acordingly
- # if rospy.has_param("<write your code here>"):
- # counter_delay_value = rospy.get_param("<write your code here>")
- # rospy.loginfo("Parameter %s was found on the parameter server. Using %fs for counter delay."%("counter_delay", counter_delay_value))
- # else:
- # rospy.loginfo("Parameter %s not found on the parameter server. Using default value of 1.0s for counter delay.","counter_delay")
- ## End of Assignment 3 - Part3
- # Variable for delay
- delay_rate = rospy.Rate(counter_delay_value)
- # Variable to decide the final state of the action server.
- success = True
- # publish info to the console for the user
- rospy.loginfo('%s action server is counting up to %i with %fs delay between each count' % (self._action_name, goal.num_counts, counter_delay_value))
- # start executing the action
- for counter_idx in range(0, goal.num_counts):
- # check that preempt has not been requested by the client
- if self._as.is_preempt_requested():
- rospy.loginfo('%s: Preempted' % self._action_name)
- self._as.set_preempted()
- success = False
- break
- # publish the feedback
- self._feedback.counts_elapsed = counter_idx
- self._as.publish_feedback(self._feedback)
- # Wait for counter_delay s before incrementing the counter.
- delay_rate.sleep()
- if success:
- self._result.result_message = "Successfully completed counting."
- rospy.loginfo('%s: Succeeded' % self._action_name)
- self._as.set_succeeded(self._result)
- if __name__ == '__main__':
- # Initialize a ROS node for this action server.
- rospy.init_node('counter_with_delay')
- # Create an instance of the action server here.
- server = CounterWithDelayActionClass(rospy.get_name())
- rospy.spin()

So, the action server.
First, we have all the relevant imports including the action definition, feedback and result message types.
And we have a Python class implementation of the action server similar to the actionlib tutorial.
So, we first define the feedback and result messages here. And then, we initialize the action server.
We give it a name, and then, we create a simple action server object which has this name, and is of type CounterWithDelay action type and processes the goal it receives in the execute callback function.
Note that this execute_cb as the same meaning as the goal callback we learned in the earlier video on ROS actions.
And let's leave the auto_start parameter as it is.
Then, we start the action server with the start function of the simple actionserver object.
Now, the execute callback function.
We have the 1s delay here and a flag to report on the result status.
We then initialize the feedback messsage and then start the actual action execution.
At first there is always a check for pre-emption of this goal and although we won't discuss it here,
we will come back to this again in Week4
where we can understand why this is necessary in a better context.
Alright, then, we update the feedback and publish it.
And after that, we wait for 1s before the next count.
Subsequently, if the goal succeeded, in this case it always will, we update the result accordingly.
Finally the main function.
We first create a ROS node for the action server called counter_with_delay.
And then, we instantiate the action server implementation
by initializing it with the name of the node.
This function get_name() actually gets the name of the ROS node
and that is exactly what will also be the name of the action server.
Note that, it is not mandatory to do it this way.
Python Action-Client:
- #! /usr/bin/env python
- from __future__ import print_function
- import rospy
- # Brings in the SimpleActionClient
- import actionlib
- # Brings in the messages used by the CounterWithDelay action, including the
- # goal message and the result message.
- from hrwros_msgs.msg import CounterWithDelayAction, CounterWithDelayGoal, CounterWithDelayResult
- def counter_with_delay_client():
- # Creates the SimpleActionClient, passing the type of the action
- # (CounterWithDelayAction) to the constructor.
- client = actionlib.SimpleActionClient('counter_with_delay', CounterWithDelayAction)
- # Waits until the action server has started up and started
- # listening for goals.
- rospy.loginfo("Waiting for action server to come up...")
- client.wait_for_server()
- num_counts = 3
- # Creates a goal to send to the action server.
- goal = CounterWithDelayGoal(num_counts)
- # Sends the goal to the action server.
- client.send_goal(goal)
- rospy.loginfo("Goal has been sent to the action server.")
- # Waits for the server to finish performing the action.
- # client.wait_for_result()
- # Does something else while the action is being done:
- for count_idx in range(0, num_counts):
- rospy.loginfo('I am doing other things while the goal is being serviced by the server')
- rospy.sleep(1.2)
- # Prints out the result of executing the action
- return client.get_result() # A CounterWithDelayResult
- if __name__ == '__main__':
- try:
- # Initializes a rospy node so that the SimpleActionClient can
- # publish and subscribe over ROS.
- rospy.init_node('counter_with_delay_ac')
- result = counter_with_delay_client()
- rospy.loginfo(result.result_message)
- except rospy.ROSInterruptException:
- print("program interrupted before completion", file=sys.stderr)

So, Action-Client
And then, we create a Simple Action Client to the counter_with_delay action server.
Then, we wait for the server to become available similar to what we did in services.
Then, we create a goal message and we send the goal to the action server from the client.
Now, like I said in the lecture video, we can include a blocking functionality in actions as well
with the wait_for_result function, but we could as well just do other things
while the action is being processed by the action server.
And lastly, we return the result we received from the action server
which contains the result of executing the goal we just sent.
And what is going on in the main function is pretty clear by now,
just the creation of the ros node for the action client,
calling the client function and some relevant log messages.
Okay, let's see, some action in action!
We start roscore then we start the action server with rosrun and we see that the server has started.
Then, we start the action client also with rosrun
and as you can see, while the goal is being processed, we can do other things!
Non-blocking execution.
We can also verify this with the feedback message.
We first echo the feedback topic
and then go back and run the action client again.
And now, you can see, there is feedback about the action running,
while the other application on the client side is also running.
And, just for completion, if we indeed wait for execution,
then we first finish the action and then do the rest of the things on the client side!
Like we see here.
4.	LAUNCHER FILES
Up until now, whenever we wanted to test our ROS nodes, we had to open up many new terminal files to run all the components.
For larger packages, this gets unwieldy really fast. This is where ROS launch files come in.
This way, we can start all our ROS nodes together in one terminal.The idea is to group ROS nodes in one file. The code for the nodes themselves is still in separate files, but we link them in one launch file, which we can launch with a single command.
It also allows for passing arguments, node specific parameters, and namespaces.
They allow for much more, but for now, we will focus our attention on the arguments and parameters.Launch files are located in the launch folder within a ROS package.
It is common practice to follow a naming convention of <package_name>_<file_name>.launch, e.g. hrwros_week1_servers.launch.Let's look at a small example.
You can see how the different nodes are started, and how the action server uses a parameter to launch.

<?xml version="1.0"?>
<launch>
    <!--Argument to the launch file-->
    <arg name="counter_delay_parameter" default="1.0"/>

    <!--Start the metres_to_feet service server ROS node-->
    <node name-"metres_to_feet" pkg="hrwros_week1" type-"metres_to_feet_server.py" output="screen"/>

    <!--Start the action server ROS node-->
    <node name="counter_with_delay" pkg-"hrwros_week1" type="counter_with_delay_as.py" output="screen">
        <param name="counter_delay" type="double" value="$(arg counter_delay_parameter)"/>
    </node>
</launch>

FIRST PROBLEM:
Your goal is to publish to and subscribe to a topic. Now, what is new about doing this? Well, in the book I used two ROS nodes, one for publisher and one for subscriber. But in this assignment, you will use only ONE ROS node for both publisher and subscriber. You will do this assignment in 3 parts, and only when you complete all 3 parts, the code will work correctly.

Let’s first set up the robotic problem we want to solve.

The recently purchased Ultrasound sensor we saw has now been installed as shown in the picture below.

The main task of this assignment is to publish a new topic that contains the height of the detected boxes based on the setup shown in the figure.

Instructions:
When there is no box, the sensor publishes the maximum range value which is the distance to theconveyor belt and it reports the distance to the top surface of the box when it does detect one.However, there is also an indication in the data sheet that, although the advertised maximum range is2.0m, the usable range is only 1.9m and any value above that is sensor noise, which means, there canbe false positives in the sensor data.So, in this part, you will MODIFYweek1_assignment1.pyto achieve the following goals:
1. Subscribe to the/sensor_infotopic.
2. Compute the height of the box from the sensor reading.3. Filter out the false positives from the sensor due to sensor noise.
Now that you have the valid height information only, you will create a new message type calledBoxHeightInformation.msg, which contains a place holder called “box_height” which is a floatingpoint number. This way you can share detected box height information with other ROS nodes in yourapplication. You can complete this part WITHOUT MODIFYINGweek1_assignment1.pyas follows:
1. Create a new message typeBoxHeightInformation.msgin the same folder whereSensorInformation.msgfile is located.
2. Add a place holderbox_heightof floating point number type in this message file.
3. Generate the new message type as instructed in the lectureUpload a screenshot of the command:> rosmsg show hrwros_msgs/BoxHeightInformation
Now, you are ready to publish a new ROS topic “/box_height_info” ONLY when a valid box isdetected. You are not supposed to publish anything when the detected box height was invalidated dueto sensor noise.You can complete this part by finishing doing the next changes on theweek1_assignment1.pyscript:
1. Create an object of the newBoxHeightInformationmessage type ONLY when you need it, thatis only when the detected box height is valid.
2. Create a publisher for the new message type in the main python module.
3. Publish the box height information on the/box_height_infotopic ONLY when the detectedbox has a valid height.Once you have finished this, and the previous two parts of the assignment, you can run the system.

To run it follow this steps:
Step 1: Start up a terminal, source your setup files, and launch therosmaster:$ roscoreNote: ALWAYS SOURCE YOUR SETUP files whenever you start a new terminal. It is assumed youwill do this all the time and this instruction will not be repeated in the future when you are asked tostart a new terminal.
Step 2: In a new terminal, start the sensor info publisher$ rosrun hrwros_week1 sensor_info_publisher.py
Step 3: In a new terminal, run theweek1_assignment1.pyscript with$ rosrun hrwros_week1 week1_assignment1.py
Step 4: In a new terminal, run the command$ rostopic list
Step 5: If you see the topic/box_height_infolisted, verify that it has a publisher with the command$ rostopic info /box_height_info
Step 6: Finally, use the command$ rostopic echo /box_height_infoAnd wait until you see 5 messages of typeBoxHeightInformation. Terminate this command withCtrl+Cand upload a screenshot of the output.